## Slide 1
CSE 4128 Image Processing and Computer Vision Laboratory Week 4: Region Descriptors and Feature Matching
Dr. Sk. Md. Masudul Ahsan
Professor
Dept. of CSE, KUET
Md Tajmilur Rahman
Lecturer
Dept. of CSE, KUET

## Slide 2: Region Descriptors
Information that lets you recognize a region.
They focus on the content and texture of objects in an image.
They describe the distribution of pixel values within a region and capture the spatial relationships between different regions.
They extract relevant information from the image and represent it in a way that can be easily compared and matched with other images.

## Slide 3: Region Descriptors
Compactness =
Form factor =
Eccentricity =
Where, a = major axis length of the bounding ellipse
b = minor axis length of the bounding

## Slide 4
0.0480
261.6433
0.4073
Form factor
Compactness
Eccentricity
0.1644
76.4262
0.00000
0.1512
83.1189
0.4340
Example

## Slide 5: Classwork
Take one of each shape as train image and the other as test image.
For each binary image:
  Find the Boundary of the object in the image.
    Apply erosion to the binary image.
    Subtract the eroded image from the binary image to get the border of the region.
  Calculate Perimeter, Area, major (a) and minor (b) axis length of the bounding ellipse of the region.
  Use Area, Perimeter, a and b the calculate Form factor, Compactness and Eccentricity.
  Matching the descriptors of the test and train images to find close Match.

## Slide 6: Erosion
1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0
1
1
1

## Slide 7: Erosion
kernel = np.ones((3,3), np.uint8)
eroded = cv2.erode(binary, kernel, iterations=1)
border = binary - eroded

## Slide 8: Parameters
Area of a region is defined as the number of pixels in the region.
area = np.count_nonzero(binary_image)
Perimeter of a region is the length of its boundary.
perimeter = np.count_nonzero(border_image)

## Slide 9: Parameters

## Slide 10: How to find axes?
contours, _ = cv2.findContours(binary, cv2.RETR_EXTERNAL, cv2.CHAIN_APPROX_SIMPLE)
cnt = max(contours, key=cv2.contourArea)
if len(cnt) >= 5:
(x, y), (MA, ma), angle = cv2.fitEllipse(cnt)

## Slide 11: Kullback-Leibler Distance

## Slide 12: Show Distance Matrix
Calculate the Kullback-Leibler Distance between each 2 images.
Create a matrix showing the similarity among each pairs.
Find which images from test cases match the most with the image from train cases.
Show the output distance matrix as a table

## Slide 13: Show as table
row_headers = [f'Test {i + 1}' for i in range(4)]
col_headers = [f'GT {i + 1}' for i in range(3)]
distances_matrix = np.array(distances_matrix)
# Display the distance matrix as a table
print(tabulate(distances_matrix[0:4,0:3], headers=col_headers, showindex=row_headers, tablefmt='grid'))

## Slide 14
 | GT1 | GT2 | GT3 | 
Test 1 | 0.0000 | 0.0049 | 0.0052 | 
Test 2 | 0.0324 | 0.0000 | 0.0030 | 
Test 3 | 0.1095 | 0.0051 | 0.0000 | 
Test 4 | 0.1480 | 0.0060 | 0.0004 | 

## Slide 15: Assignment: Hu Moments
1
2
3
4
5
7
6
Derivation of these results requires concepts that are beyond the scope of this discussion. The book by Bell [1965] and the paper by Hu [1962] contain detailed discussions of these concepts. For generating moment invariants of an order higher than seven, see Flusser [2000]. Moment invariants can be generalized to n dimensions (see Mamistvalov [1998]).

## Slide 16: Hu Moments
This set of moments is invariant to translation, scale change, mirroring (within a minus sign), and rotation.
We can attach physical meaning to some of the low-order moment invariants.
  For example, 1 is the sum of two second moments with respect to the principal axes of data spread, so this moment can be interpreted as a measure of data spread.
  Similarly, 3 is the difference of second moments, and may be interpreted as a measure of “slenderness.”
  However, as the order of the moment invariants increases, the complexity of their formulation causes physical meaning to be lost.

## Slide 17: Hu Moments

## Slide 18: Hu Moments

## Slide 19: Assignment